## Slide 1: Using the FLIR 6 Thermal Image Camera
Sand Hutton and Claxton Village Hall
Saturday 24th February 2024
Philip Orton

## Slide 2: Surveying Manor House –built pre 1900

## Slide 3: Mainly solid wall- extension has a cavity wall(red) Energy Performance Certificate (EPC) E 50 points

## Slide 4: Selecting the camera Hot spot function to detect external heat loss………

## Slide 5: Bright spots indicate heat loss.......

## Slide 6: There is noticeable heat loss under bay window…..

## Slide 7: Moving inside to bay window….

## Slide 8: And changing camera setting to detect Cold spot…

## Slide 9: -shows corresponding cold zone under window …..

## Slide 10: The house north wall, which gets little sun; the 1973 extension is to the right….a cold wall

## Slide 11: Inside this north wall is a dining room.. with inset left and right alcoves…

## Slide 12: - alcove walls show up as a cold spot……

## Slide 13: - an insulation job beckons……!

## Slide 14: Success!- reduced heat loss from insulated left alcove compared to uninsulated on the right…

## Slide 15: Outside again, the right hand north wall extension shows a hot spot …

## Slide 16: -this contains the bathroom, which seems to have some condensation patches on the ceiling…..

## Slide 17: with associated cold spots……..

## Slide 18: There is little insulation in the ceiling space here….

## Slide 19: - which has been improved to current standards…….

## Slide 20: -but there are still some problems with loft hatch drafts…

## Slide 21: Rolling out the camera to the community Anne shows off her door insulation……….

## Slide 22: The thermal image shows the benefit of the insulation and the covering curtain…..

## Slide 23: A little of the science behind thermography..